## Slide 1
Cape Code
Dakota Myers

## Slide 2: Cape Cod Architecture
Early American settlers developed this Northeastern U.S. style, which is known for its gabled roof and plain front
Next time you play Monopoly, take a look at the little green house you put down on Park Place. With its steep roof, central chimney and rectangular shape, the game piece is a good, albeit tiny, example of a classic Cape Cod home.

## Slide 3
The big, central chimney was literally the heart of the home: It provided heat to all the rooms clustered around it, as well as light and, of course, dinner. Cedar shingles on the exterior and the roof also helped cut the cold. A steep roof quickly shed rain and snow. Everything about the Cape Cod style was adopted for its function rather than its form.

## Slide 4: Key Elements
Large, central chimney. The large, central chimney is located directly behind the front door, with the rooms clustered around it in a rectangular shape.
Steep roof. Cape Cods have steep roofs to quickly shed rain and snow, and a shallow roof overhang.
Windows and dormers. A full Cape has two windows on each side of the door, and often has a dormer on each side of the chimney to open up the attic.
Captain's stairway. "The second floor, often kept for boarders or 'seafaring' men, was accessed by a narrow stair, or 'captain's stairway,' which has incredibly steep risers and shallow treads to minimize the use of the first-floor space," explains David Karam, an architect and builder from Brewster, Mass.
Shingle siding. Weathered gray shingles are one of the most recognizable elements of a classic Cape Cod, but newer homes are built of brick, stucco and stone.

## Slide 5: References
http://www.frontdoor.com/home-styles/cape-cod-architecture